## Slide 1
Embedded System
(Sistem tertanam)
Pertemuan II :
Pendahuluan
Oleh: M. Priyono Tri Sulistyanto, S.T., M.Eng

## Slide 2
Materi Kuliah
2
Kontrak Kuliah
Pendahuluan
Arduino
Embedded Debugging
ATmega328P
GPIO (General Purpose Input/Output)
Time Ports
Interrupt Processing
Serial Communication
Non-Volatile Memory
Example Project 1
Example Project 2
Example Project 3
Example Project 4
Embedded System (Teknik Informatika)

## Slide 3
Embedded System?
3
An embedded system is a computer system with a dedicated function within a larger mechanical or electrical system, often with real-time computing constraints.
Embedded System (sistem tertanam) adalah sistem komputer dengan fungsi yang khusus didalamnya terdapat sistem elektonik atau mekanik yang besar, seringkali dengan batasan berupa komputasi real time
Embedded System (Teknik Informatika)

## Slide 4
Karakteristik Embedded System
4
Embedded System (Teknik Informatika)
Menjadi bagian dari sistem yang lebih besar
Application-specific, bahkan sebagian bekerja dengan real-time.
Baik hardware maupun software dirancang khusus untuk aplikasi yang spesifik.)
Interaksi dengan dunia fisik

## Slide 5
Embedded System
5
Embedded System (Teknik Informatika)
Biaya (cost) -> cost effective hardware
Constraint waktu -> mostly real-time application
Interaksi langsung dengan dunia nyata
Constraint energi -> low power
Elektronika

## Slide 6
Embedded System v.s Dekstop Computer
6
Embedded System (Teknik Informatika)
Embedded | Desktop
Fungsi khusus | Fungsi umum
Banyak pilihan prosesor (dari 8 bit sampai 64 bit) | Pilihan prosesor terbatas (Pentium, AMD, PowerPC dsb)
Cost sensitive (harus murah) | Sedikit Mahal
Real time | 
Operating System umumnya real-time OS / RTOS | Operating System umumnya tidak harus real-time OS : Unix, windows
Kegagalan sistem umumnya berakibat serius | Kegagalan tidak berakibat fatal

## Slide 7
Embedded System v.s Dekstop Computer
7
Embedded System (Teknik Informatika)
Embedded | Desktop
Daya terbatas (batere, solar cell) | Daya dari jala-jala
Sering dioperasikan pada tempat yang alamnya kurang bersahabat: Luar angkasa , Tengah laut, Tempat dingin/panas | Sering dioperasikan di tempat yang alamnya bersahabat
Sumber daya terbatas : RAM, ROM, CPU | Sumber daya banyak: RAM besar ,ROM besar, CPU cepat
Program disimpan di ROM | Program disimpan di hard disk / magnetic media

## Slide 8
Embedded System in every where
8
Embedded System (Teknik Informatika)

## Slide 9
Embedded System in every where
9
Embedded System (Teknik Informatika)
Kendali proses:
Food processing (pabrik)
Chemical plants (pabrik)
Otomotif
Engine control
Antilock braking system
Pesawat Terbang
Kereta Api
Telekomunikasi
Office Automation
FAX machine
Copiers
Computer Peripherals
Printer
Terminal
Disk drive
Modem
Scanner
Mouse (optical)

## Slide 10
Embedded System in every where
10
Embedded System (Teknik Informatika)

## Slide 11
Embedded System in every where
11
Embedded System (Teknik Informatika)
Communication
Switches
Routers
Robot
Aerospace
Flight management System
Weapons Systems
Jet engine controls
Domestic
Microwave oven
Dishwashers
Washing machines
thermostats

## Slide 12
Embedded System in every where
12
Embedded System (Teknik Informatika)
Buoy di laut dengan sensor lingkungan

## Slide 13
Embedded System in every where
13
Embedded System (Teknik Informatika)
Consumer Electronic
Pabrik (proses kimia)

## Slide 14
Embedded System in every where
14
Embedded System (Teknik Informatika)
Robot

## Slide 15
Embedded System in every where
15
Embedded System (Teknik Informatika)
Multiprocessor
  8-bit/32-bit for UI
  DSP for signals
  32-bit in IR port
  32-bit in Bluetooth
8-100 MB of memory
All custom chips
Power consumption & battery life depends on software
Telepon bergerak

## Slide 16
Embedded System in every where
16
Embedded System (Teknik Informatika)
Massive signal processing
  Several processing tasks per connected mobile phone
Based on DSPs
  Standard or custom
  100s of processors

## Slide 17
Embedded System in every where
17
Embedded System (Teknik Informatika)
Massive signal processing
  Several processing tasks per connected mobile phone
Based on DSPs
  Standard or custom
  100s of processors